## Slide 1: Running in Batch Mode
Yongsheng.guo@ansys.com
2021-12-15
Note: This version is under test and not be released yet

## Slide 2: How to set Parameters
There are three positions where importing parameters can be set
  Configure file: tech2xmlOption.json, this file will be generated if not exist under the folder of “GDSImportWizard.py” when running the wizard.
  Using system environment variables
  Set the parameters in command arguments.
These three methods can achieve the same effect, but with different priorities.
Notes: 三种方式可以达到相同的效果，优先级不同。

## Slide 3: Priorities
tech2xmlOption.json
System environment
Command arguments
Priorities High
If the same parameter given in multiple places, the higher priority parameter will take precedence.
As one example, if one parameter is given in System environment and tech2xmlOption.json at the same time, System environment value will have high priorities and take precedence.
GUI Interface have the highest priority, Command arguments System environment and tech2xmlOption.json setting will be used as initial values of GUI input elements.
GUI Interface

## Slide 4: Parameters
Parameters |  | Defalut Value |  | Description
Technology Parameters |  |  |  | 
InputType | 0 | 0 | 0: Ircx, others: not define | 0: Ircx, others: not define
UseShortMergeLayerName | TRUE | TRUE | changing is not recommended | changing is not recommended
SimplifyDieletricMethod | 1, | 1, | 0: NoSimplify, No Merge on Dielectric, exact layers in IRCX 1 : MergeThinLayer, Merge layer thinner than a specific value 2:BlockMerge, use average DK on all layers except substrate | 0: NoSimplify, No Merge on Dielectric, exact layers in IRCX 1 : MergeThinLayer, Merge layer thinner than a specific value 2:BlockMerge, use average DK on all layers except substrate
MergeDielectricMethod | 0 | 0 | 0: Weighted Average 1: Weighted Average 2: Kraszewski equation 3: Landau equation 4: Lichtenecker equation | 0: Weighted Average 1: Weighted Average 2: Kraszewski equation 3: Landau equation 4: Lichtenecker equation
ThinDielectricThreshold | 0.1 | 0.1 | 0.1: Merge layer when layer thickness<0.1um, default unit um | 0.1: Merge layer when layer thickness<0.1um, default unit um
DkDeviationThreshold | 0.05 or 5% | 0.05 or 5% | 0.05: Merge layers when dk difference less then 10% | 0.05: Merge layers when dk difference less then 10%
FixedSmallLayerGap | 0.005 | 0.005 | 0.005: Fix small air gap between layers less then 0.005um, default unit um | 0.005: Fix small air gap between layers less then 0.005um, default unit um
UseDefaultDF | TRUE | TRUE | True: If not hav df value in technology, a default df value will be used false: If not hav df value in technology, will set df =0 | True: If not hav df value in technology, a default df value will be used false: If not hav df value in technology, will set df =0
DefaultDF | 0.02 | 0.02 | set for default df value | set for default df value
NotUseDfonSubstrate | TRUE | TRUE | True: default df value will never used on Substrate layer(Silicon material), it is recommended to set as True. | True: default df value will never used on Substrate layer(Silicon material), it is recommended to set as True.
UseSheetLayer | TRUE | TRUE | True: set the layers as 0um when it small then "SheetLayerThreshold", which will avoid to generatelarge number of tiny meshes | True: set the layers as 0um when it small then "SheetLayerThreshold", which will avoid to generatelarge number of tiny meshes
SheetLayerThreshold | 0.0015 | 0.0015 | 0.0015: if "UseSheetLayer" is True, layers which < 0.0015um will set to zero thickness(treat as 2D sheet object) | 0.0015: if "UseSheetLayer" is True, layers which < 0.0015um will set to zero thickness(treat as 2D sheet object)
CreatViaGroups | TRUE | TRUE | True: ViaGroups will be implemented on via layers | True: ViaGroups will be implemented on via layers
IgnoreLayersReg | “air, ctm.*,cbm.*,dtce.*" | "air,ctm.*,cbm.*"dtce.*" | layers will not import into 3D Layout. Regular expressions are used, and ignoreLayerNames are seprate with comma or space | layers will not import into 3D Layout. Regular expressions are used, and ignoreLayerNames are seprate with comma or space
TextLayermap | None | None | text layers indicate for net extraction, None will use all text layer in technoloyg files. User could set it accrond the rule: "ubmb:125:100, "ubump:125:0" | test layers indicate for net extraction, None will use all text layer in technoloyg files. User could set it accrond the rule: "ubmb:125:100, "ubump:125:0"
InsulatorThickness | 1 | 1 | if not described in in technoloyg files, default TSV insulation thickness, unit in um. | if not described in in technoloyg files, default TSV insulation thickness, unit in um.

## Slide 5: Parameters
Parameters |  | Defalut Value |  | Description
Path Parameters |  |  |  | 
TechFile | None | None | input: techFile path (Absolute), must set | input: techFile path (Absolute), must set
LayerMapFile | None | None | input: layerMapFile path (Absolute), not used | input: layerMapFile path (Absolute), not used
GdsFile | None | None | input: gdsFile path (Absolute), must set | input: gdsFile path (Absolute), must set
AedtInstallDir | None | None | input: AEDT installtion path (Absolute), must set to do edb post | input: AEDT installtion path (Absolute), must set to do edb post
ControlXmlPath | None | None | output: controlXmlPath (Absolute), optional | output: controlXmlPath (Absolute), optional
edbPath | None | None | output: edbPath (Absolute), optional | output: edbPath (Absolute), optional
Gds post Parameters |  |  |  | 
OpenInAedt | True | True | true: will open EDB when the conversion is completed | true: will open EDB when the conversion is completed
AutoComps | True | True | true: will automatic generation device, easy port creation | true: will automatic generation device, easy port creation
CompLayerList | "1,-1" | "1,-1" | index for which layers will generate components, 1 indicate top layer, -1 indicate bottom layer, and so on. | index for which layers will generate components, 1 indicate top layer, -1 indicate bottom layer, and so on.
AutoTSVCoat | True | True | true: will automatic generation tsv insulator | true: will automatic generation tsv insulator
DissolveViaGroup | True | True | true: dussikve all groups or component before doing edb post processing | true: dussikve all groups or component before doing edb post processing
UseTemperatureDependMaterial | True | True | true: will generate temperature dependance materail if TC1/TC2 given in material defintion | true: will generate temperature dependance materail if TC1/TC2 given in material defintion

## Slide 6: Running in windows command line

## Slide 7: Running in batch mode - Windows
Eg1. Configure from system environment:
  set AedtInstallDir=C:\Program Files\AnsysEM\AnsysEM21.1\Win64
  set GdsFile=D:\HFSS\GDSII\GDS2XML\TECH2XML_test\test.gds
  set TechFile=D:\HFSS\GDSII\GDS2XML\TECH2XML_test\TSMC_INTERPOSER.ircx
  set path=% AedtInstallDir %\common\IronPython;%path%
  ipy64 GDSImportWizard.py -batch
Eg2. Configure from command arguments:
  set AedtInstallDir=C:\Program Files\AnsysEM\AnsysEM21.1\Win64
  set path=% AedtInstallDir %\common\IronPython;%path%
  ipy64 GDSImportWizard.py –GdsFile “D:\HFSS\GDSII\GDS2XML\TECH2XML_test\test.gds” – TechFile “D:\HFSS\GDSII\GDS2XML\TECH2XML_test\TSMC_INTERPOSER.ircx”
Note: system environment and command arguments could be mixed.
Notes: ipy64 D:\Study\Script\repository\HFSS\GDSII\GDS2XML\GDSTranslator\GDSTranslator\Program.py -TechFile "D:\HFSS\GDSII\GDS2XML\TECH2XML_test\TSMC_INTERPOSER.ircx“ -GdsFile "D:\HFSS\GDSII\GDS2XML\TECH2XML_test\test.gds"

## Slide 8: Running in batch mode - Windows
A short command is supported:
  ipy64 GDSImportWizard.py gdspath
  ipy64 GDSImportWizard.py gdspath edbpath
Eg3. short command
  ipy64 GDSImportWizard.py “D:\HFSS\GDSII\GDS2XML\TECH2XML_test\test.gds” –TechFile “D:\HFSS\GDSII\GDS2XML\TECH2XML_test\TSMC_INTERPOSER.ircx”

## Slide 9: Running in Linux

## Slide 10: Running in batch mode - Linux
Eg1. Configure from system environment:
  export AedtInstallDir='/home/ansys/app/AnsysEM20.1/Linux64'
  export GdsFile=/home/ansys/yguo/test/test.gds
  export TechFile=/home/ansys/yguo/test/TSMC_INTERPOSER.ircx
  export ipy64="$AedtInstallDir /common/mono/Linux64/bin/mono $AedtInstallDir /common/IronPython/ipy64.exe"
  $ipy64 GDSImportWizard.py
Eg2. Configure from command arguments:
  export AedtInstallDir='/home/ansys/app/AnsysEM20.1/Linux64'
  export ipy64="$AedtInstallDir /common/mono/Linux64/bin/mono $AedtInstallDir /common/IronPython/ipy64.exe"
  $ipy64 GDSImportWizard.py –GdsFile “D:\HFSS\GDSII\GDS2XML\TECH2XML_test\test.gds” – TechFile “D:\HFSS\GDSII\GDS2XML\TECH2XML_test\TSMC_INTERPOSER.ircx”
Note: system environment and command arguments could be mixed.
Notes: ipy64 D:\Study\Script\repository\HFSS\GDSII\GDS2XML\GDSTranslator\GDSTranslator\Program.py -TechFile "D:\HFSS\GDSII\GDS2XML\TECH2XML_test\TSMC_INTERPOSER.ircx“ -GdsFile "D:\HFSS\GDSII\GDS2XML\TECH2XML_test\test.gds"

## Slide 11: Running in batch mode - Linux
A short command is supported:
  ipy64 GDSImportWizard.py gdspath
  ipy64 GDSImportWizard.py gdspath edbpath
Eg3. short command
  export AedtInstallDir='/home/ansys/app/AnsysEM20.1/Linux64'
  export ipy64="$aedtInstallPath/common/mono/Linux64/bin/mono $aedtInstallPath/common/IronPython/ipy64.exe"
  $ipy64 GDSImportWizard.py “D:\HFSS\GDSII\GDS2XML\TECH2XML_test\test.gds” – TechFile “D:\HFSS\GDSII\GDS2XML\TECH2XML_test\TSMC_INTERPOSER.ircx”